## Slide 1: Incident Summary for CCE
November 2018-current

## Slide 2: Overview of Incidents
Incident Type | Total for Current Quarter | Total for 2018 Academic Year
Equipment related | 2 | 2
Chemical Exposures | 2 | 2
Chemical Spills | 1 | 2
Injuries | 0 | 0
Fires | 0 | 0
Current Quarter: 11/2018 to current
2018 Academic Year: 9/2018 to current

## Slide 3: Equipment Related
Liquid nitrogen valve partially stuck open: After dispensing liquid nitrogen, valve was difficult to fully close so there was a small leak
-Lab was eventually able to close valve
  -A few of these occurred on the same day in different labs, right after raining. Humidity levels were very high
  -Can use heat gun on valve if leak is slow and no danger of asphyxiation or contact with leaking nitrogen. Call Safety for assistance
  -If leak is large, evacuate lab area and call x5000
  False alarm, phosphine: Phosphine alarm sounded, likely tripped due to construction dust. Building was evacuated
  -Phosphine not being used in lab, so alarm was shut off

## Slide 4: Chemical Exposures
Potential inhalation of triethylamine: Graduate student felt dizzy after experiencing a ‘fishy’ smell coming from a shared rotovap. Student felt OK after getting fresh air.
-Shared rotovap had an issue with the vacuum system that caused a leak, issue was not communicated to other lab members
-Lab members must communicate to others when shared equipment has issues.
-Lab discussed posting signage if equipment is out of order
Minor sulfuric acid exposure: a student was exposed to splattered material generated from a reaction of sucrose with sulfuric acid when they moved to the side of a blast shield. This resulted in minor burns.
-Student’s inexperience coupled with the nature of this experiment may require additional controls to prevent exposure
-Incident reporting and internal communication procedures are being evaluated and reinforced

## Slide 5: Chemical Spill
Spill of acryloyl chloride: Lab members experienced lachrymating odor in the lab. Lab evacuated and found a cracked bottle of acryloyl chloride in a refrigerator had leaked. Lab secured area then called Security.
-Bottle cracked because this monomer polymerized, likely generating pressure and/or heat
-Even though spill size was small (~50 mL) this was an emergency because respiratory protection was required to clean it (toxic vapor, lachrymator). Labs should not clean spills requiring a respirator
-Bottle was not in secondary containment, causing spill to spread
-Potentially sensitive monomers should be labeled with date of receipt to ensure old or potentially compromised bottles are disposed of (even with stabilizer)